This is part of Family API which allow to create dual-os version of program runs under OS/2 and DOS
Note: This is legacy API call. It is recommended to use 32-bit equivalent
# DosExit
This call is issued when a thread completes executing. The current thread or process ends.
##### Syntax
DosExit (ActionCode, ResultCode)
##### Parameters
ActionCode (USHORT) - input : Terminates the process and all its threads.
Value	Definition
0	The current thread ends.
1	All threads in the process end.

ResultCode (USHORT) - input : Program's completion code. It is passed to any thread that issues DosCwait for this process.
##### Remarks
DosExit allows a thread to terminate itself or be terminated by another thread in its process. If ActionCode=0 and the specified thread is the last thread executing in the process, or if ActionCode=1, the process terminates.
The system can start threads on behalf of an application. Thus, if the intent of a DosExit call is to terminate the process, ActionCode=1 should be specified to terminate all the threads belonging to the process.
Do not terminate thread 1 without terminating the process. Thread 1 is the initial thread of execution, not a thread started by a DosCreateThread request. When thread 1 ends, any monitors or signal processing routines set for this process also end. To avoid unpredictable results, DosExit should be specified with ActionCode=1 to ensure the process ends.
When a process is terminating, all but one thread is terminated and that thread executes routines whose addresses have been specified with DosExitList. After resources have been cleaned up by the exit list routines, this thread and all other resources owned by the process are released.
#### Family API Considerations
Some options operate differently in the DOS mode than in the OS/2 mode. Therefore, the following restrictions apply to DosExit when coding for the DOS mode:
- There is no thread support in DOS 3.3; therefore DosExit exits the currently executing program.
- If ActionCode = 0 this option is ignored. It is equivalent to an ActionCode = 1.
##### Example Code
#### C Binding
#define INCL_DOSPROCESS
VOID DosExit(ActionCode, ResultCode);
USHORT ActionCode; /* Indicates end thread or process */
USHORT ResultCode; /* Result Code to save for DosCwait */
In this example, the main routine starts up another program, simple.exe, and then expects a return code of 3 to be returned. Simple.exe sets the return code with DosExit.
#define INCL_DOSPROCESS
#define START_PROGRAM "simple.exe"
#define RETURN_OK 3
CHAR LoadError[100];
PSZ Args;
PSZ Envs;
RESULTCODES ReturnCodes;
USHORT rc;
   if(!DosExecPgm(LoadError, /* Object name buffer */
        sizeof(LoadError), /* Length of object name buffer */
        EXEC_SYNC, /* Asynchronous/Trace flags */
        Args, /* Argument string */
        Envs, /* Environment string */
        &ReturnCodes, /* Termination codes */
        START_PROGRAM)) /* Program file name */
      if (ReturnCodes.codeResult == RETURN_OK) /* Check result code */
        printf("things are ok..");
      else
        printf("something is wrong...");
—————-simple.exe——————
#define INCL_DOSPROCESS
#define RETURN_CODE 3
main( )
   {
   printf("Hello!\n");
   DosExit(EXIT_THREAD, /* End thread/process */
        RETURN_CODE); /* Result code */
   }
The following example shows how to suspend and resume execution of a thread within a process. The main thread creates Thread2 and allows it to begin executing. Thread2 iterates through a loop that prints a line and then sleeps, relinquishing its time slice to the main thread. After one iteration by Thread2, the main thread suspends Thread2 and then resumes it. Subsequently, Thread2 completes the remaining three iterations.
#define INCL_DOSPROCESS
#include <os2.h>
#define SEGSIZE 4000 /* Number of bytes requested in segment */
#define ALLOCFLAGS 0 /* Segment allocation flags - no sharing */
#define SLEEPSHORT 5L /* Sleep interval - 5 milliseconds */
#define SLEEPLONG 75L /* Sleep interval - 75 milliseconds */
#define RETURN_CODE 0 /* Return code for DosExit() */
VOID APIENTRY Thread2()
{
  USHORT i;
  /* Loop with four iterations */
  for(i=1; i<5; i++)
  {
    printf("In Thread2, i is now %d\n", i);
    /* Sleep to relinquish time slice to main thread */
    DosSleep(SLEEPSHORT); /* Sleep interval */
  }
  DosExit(EXIT_THREAD, /* Action code - end a thread */
        RETURN_CODE); /* Return code */
}
main()
{
  TID ThreadID; /* Thread identification */
  SEL ThreadStackSel; /* Segment selector for thread stack */
  PBYTE StackEnd; /* Ptr. to end of thread stack */
  USHORT rc;
  /** Allocate segment for thread stack; make pointer to end of stack. **/
  /** We must allocate a segment in order to preserve segment **/
  /** protection for the thread. **/
  rc = DosAllocSeg(SEGSIZE, /* Number of bytes requested */
        &ThreadStackSel, /* Segment selector (returned) */
        ALLOCFLAGS); /* Allocation flags - no sharing */
  StackEnd = MAKEP(ThreadStackSel, SEGSIZE-1);
  /** Start Thread2 **/
  if(!(rc=DosCreateThread((PFNTHREAD) Thread2, /* Thread address */
        &ThreadID, /* Thread ID (returned) */
        StackEnd))) /* End of thread stack */
    printf("Thread2 created.\n");
  /* Sleep to relinquish time slice to Thread2 */
  if(!(DosSleep(SLEEPSHORT))) /* Sleep interval */
    printf("Slept a little to let Thread2 execute.\n");
  /***** Suspend Thread2, do some work, then resume Thread2 *****/
  if(!(rc=DosSuspendThread(ThreadID))) /* Thread ID */
    printf("Thread2 SUSPENDED.\n");
  printf("Perform work that will not be interrupted by Thread2.\n");
  if(!(rc=DosResumeThread(ThreadID))) /* Thread ID */
    printf("Thread2 RESUMED.\n");
  printf("Now we may be interrupted by Thread2.\n");
  /* Sleep to allow Thread2 to complete */
  DosSleep(SLEEPLONG); /* Sleep interval */
}
#### MASM Binding
EXTRN DosExit:FAR
INCL_DOSPROCESS EQU 1
PUSH WORD ActionCode ;Indicates end thread or process
PUSH WORD ResultCode ;Result Code to save for DosCwait
CALL DosExit
#### Note
This text based on http://www.edm2.com/index.php/DosExit_(FAPI)
Family API
DOS	Process Manager	DosBeep DosExit DosSleep DosExecPgm
File Manager	DosChDir DosChgFilePtr DosClose DosDelete DosDupHandle DosMkDir DosMove DosQCurDir DosQCurDisk DosSetFileMode DosOpen DosQFileInfo DosRead DosQFileMode DosQFSInfo DosQVerify DosRmDir DosSelectDisk DosFindClose DosFindFirst DosFindNext DosSetFileInfo DosSetVerify DosWrite DosFileLocks DosSetFHandState DosNewSize DosBufReset DosQFHandState DosSetFSinfo
Memory Manager	DosFreeSeg DosSubAlloc DosSubFree DosSubSet DosAllocHuge DosAllocSeg DosReallocHuge DosReallocSeg DosGetHugeShift DosCreateCSAlias
NLS	DosCaseMap DosGetCtryInfo DosGetDBCSEv DosSetCtryCode DosGetCollate DosGetMessage DosInsMessage DosPutMessage
Date and Time	DosSetDateTime DosGetDateTime
Devices	DosDevConfig DosDevIOCtl DosDevIOCtl2
Signals	DosHoldSignal DosSetSigHandler
Misc	BadDynLink DosGetEnv DosGetMachineMode DosGetVersion DosError DosErrClass DosSetVec
KBD		KbdCharIn KbdFlushBuffer KbdGetStatus KbdSetStatus KbdStringIn KbdPeek
VIO		VioGetBuf VioGetConfig VioGetCurPos VioGetCurType VioGetPhysBuf VioReadCellStr VioReadCharStr VioScrollUp VioScrollDn VioScrollLf VioScrollRt VioScrUnLock VioSetCurPos VioSetCurType VioSetMode VioGetMode VioShowBuf VioWrtCellStr VioWrtCharStr VioWrtCharStrAtt VioWrtNAttr VioWrtNCell VioWrtNChar VioWrtTTY VioScrLock VioPopUp
Tools		BIND
Modules		DOSCALLS.DLL VIOCALLS.DLL KBDCALLS.DLL MSG.DLL
Libraries		API.LIB OS2386.LIB FAPI.LIB DOSCALLS.LIB SUBCALLS.LIB