### Initial memory map
The standard PC has the following memory map:
Addresses	Name	Description
0x000000-0x09FFFF	Conventional memory	RAM, which can be used by user
0x0A0000-0x0BFFFF	Video memory	RAM, used by video adapter
0x0C0000-0x0CFFFF	Adapter's ROM	ROM, used by different adapters
0x0D0000-0x0DFFFF	Page Frame	RAM used to map Expanded memory
0x0E0000-0x0FFFFF	BIOS	PC BIOS ROM

Conventional memory mapped as:
Addresses	Name	Description
0x000000-0x0003FF	Interrupt Vectors	This memory used to control Inerrupts
0x000400-0x0004FF	BIOS Data Area	Used by ROM BIOS

#### After BIOS POST
Addresses	Name	Description
0x000000-0x0003FF	Interrupt Vectors	This memory used to control Inerrupts
0x000400-0x0004FF	BIOS Data Area	Used by ROM BIOS
0x000500-0x007BFF	Free	Free, unused memory
0x007C00-0x007DFF	MBR
0x007E00-0x09FFFF	Free Conventional memory	RAM, which can be used by user
0x0A0000-0x0BFFFF	Video memory	RAM, used by video adapter
0x0C0000-0x0CFFFF	Adapter's ROM	ROM, used by different adapters
0x0D0000-0x0DFFFF	Page Frame	RAM used to map Expanded memory
0x0E0000-0x0FFFFF	BIOS	PC BIOS ROM

### After MBR
This information correct for our MBR
Addresses	Name	Description
0×000000-0x0003FF	Interrupt Vectors	This memory used to control Inerrupts
0×000400-0x0004FF	BIOS Data Area	Used by ROM BIOS
0×000500-0x0005FF	Free	Free, unused memory
0×000600-0x0007FF	MBR	Master Boot Record
0×000800-0x007BFF	Free	Free, unused memory
0x007C00-0x007DFF	Boot record	Boot Record loaded from boot sector of active partition
0x007E00-0x007FFF	MBR Work area	This area was used as MBR work area
0×008000-0x09FFFF	Free Conventional memory	RAM, which can be used by user
0x0A0000-0x0BFFFF	Video memory	RAM, used by video adapter
0x0C0000-0x0CFFFF	Adapter's ROM	ROM, used by different adapters
0x0D0000-0x0DFFFF	Page Frame	RAM used to map Expanded memory
0x0E0000-0x0FFFFF	BIOS	PC BIOS ROM

### After boot record
This information correct for our bootsector
Addresses	Name	Description
0×000000-0x0003FF	Interrupt Vectors	This memory used to control Inerrupts
0×000400-0x0004FF	BIOS Data Area	Used by ROM BIOS
0×000500-0x0005FF	Free	Free, unused memory
0×000600-0x0007FF	MBR	Master Boot Record
0×000800-0x007BFF	Free	Free, unused memory
0x007C00-0x007DFF	Boot record	Boot Record loaded from boot sector of active partition
0x007E00-0x007FFF	Boot record Work area	This area was used as Boot Record work area
0×008000-(MuFSDStart-1)	Free	Free, unused memory
MuFSDStart-MuFSDEnd	MicroFSD	MicroFSD/BlackBox code
(MuFSDEnd+1)-0x09FFFF	Free Conventional memory	RAM, which can be used by user
0x0A0000-0x0BFFFF	Video memory	RAM, used by video adapter
0x0C0000-0x0CFFFF	Adapter ROMs	ROMs, used by different adapters
0x0D0000-0x0DFFFF	Page Frame	RAM used to map Expanded memory
0x0E0000-0x0FFFFF	BIOS	PC BIOS ROM

MuFSDStart=0×008000 or 0×090000. Now we use 0×090000 as LILO does but have a plan to use 0×008000 for more compact memory reuse and less possibility of overlapping.
MuFSDEnd is (0×008000+MicroFSD_file_length-1)
### After MicroFSD/BlackBox
Memory map after MicroFSD/BlackBox work known via MemoryMap structure.
### After FreeLDR
Memory map after FreeLDR work known via Multiboot Information block.
### After L4Ka::Kickstart
Memory map after L4Ka:Kickstart work known to microkernel via Kernel Interface Page. Other tasks has access to memory via sigma0 server. Strating from this point all memory operation controlled by L4 microkernel.
#### Discussion